### STANDARD SPECIFICATIONS

### THERMOSTOP BENTLEY

### Section 08362: Sectional Metal Overhead Doors

#### PART 1 – GENERAL

  - Works by others:

- Metal fabrication, section 05500

- Electrical power supply, division 16

- Structural work, division 5

  - Construction requirements:

- Design doors to withstand wind load of 21 psf with a maximum horizontal deflection of 1/120 of opening width

- ASTM E-283 (air leakage): less than 0.130 cfm/ft2  at 25 miles/hour

- ASTM E-547 (water penetration): absolutely no leak

  - Shop drawing: Supply shop drawings in accordance with plans and specifications for approval. Contractor shall be responsible for job site dimensions before fabrication and co-ordination with others sub-trades.

  - Maintenance instructions: Supply maintenance instructions for hardware and/or others components in accordance section 01300.

  - Warranty: Thermostop doors and hardware carry a warranty of one (1) year against any defect or faulty workmanship. The door panels carry a ten (10) year limited warranty against perforation due to rusting, and a five (5) year limited warranty on delamination, under normal operational conditions.

#### PART 2 - PRODUCT

  - Material:

- Pre-painted galvanised G-60 metal sheet conform to ASTM A653

- Commercial aluminium extrusions  6063 T5

- Insulation: foamed in place polyurethane, 2.56 lbs/ft3 (41.0 kg/m3) minimum density, conform to 
CGSB 51-GP-21M.

  - Reference product: Thermostop Bentley, as manufactured by THERMOSTOP INC., 3775 Losch boulevard, Longueuil, (Québec),  Canada, Tel.: 450-678-8666, Fax: 450-678-7765, www.thermostop.com

  - Dimensions and clearances:

Quantity 			Dimensions				Clearances

(height x length)				(floor to first obstruction)

  - Panel manufacturing process: The inner core consists of rigid polyurethane, foamed in place under high pressure between two metal skins. The panel is equipped, on its full length, with 20ga. steel (0.86mm) continuous reinforcement plates, for the solid attachment of hinges. To avoid mouldiness, no wood material is used in the construction of the panel.

  - Insulation: CFC-free rigid foamed-in-place polyurethane. 2.56 lbs/ft3 (41.0 kg/m3) minimum density . Insulation value is equal to R-8 per inch (25,4mm) thickness of insulated panel.

  - Joint and seal: High quality galvanized steel skins roll formed into an exclusive tongue-and-groove joint with a true thermal break and a double bubble-shaped weather seal (single seal for the Mark II models).

  - Thermal break: To eliminate all possibilities of thermal conductivity, a true thermal break of ¾” (18mm) for the 2” thick door separates the exterior skin from the interior one.

  - Metal skins and thickness:

Option available: 20ga. Steel: Thermostop Bentley 2” thick

  - Finish: 20ga. Steel: White, optional shop painted color. Smooth finish, with ribs.

  - Window or full view panel:

- Type A: full view extruded aluminum panel, with clear 1/8" (3mm) - 1/8" (3mm) thermal sealed glass.

- Type B: square corner black frame. Double acrylic or clear 1/8" (3mm) - 1/8" (3mm) thermal sealed glass. Standard 24” (610mm) x 12” (305mm).

- Type E: square corner white frame. Clear 1/8" (3mm) - 1/8" (3mm) thermal sealed glass. Standard 24” (610mm) x 12” (305mm).

Optional: tempered glass, tinted glass, lexan.

  - Perimeter weather seal: triple-lip, flexible PVC weather seal, retained in an extra robust extruded aluminum retainer.

  - Bottom weather seal: U-shaped, flexible PVC double weather seal, retained in a heavy duty extruded aluminum retainer, securely fastened to the bottom of the door (one bottom seal for the Mark II models).

  - End caps: Sections are equipped with 16ga. (1.42mm) thick galvanized steel end caps.

#### PART 3 – HARDWARE

High quality 2” hardware, model 50-T.

- Tracks: 2” (50mm) vertical and horizontal tracks formed from 14ga. (1.80mm) thick galvanized steel. Vertical tracks shall be taper-mounted for a "wedge-tight" closing.

- Rollers: 2” (50mm) in diameter and equipped with 1/4” (6mm) diameter ball bearings running in hardened inner and outer racers. Roller stem shall be heavy cold rolled steel.

- Hinges: 13ga. (2.10mm) thick galvanized steel graduated to ensure a weather tight closing at the jambs. Door with width greater than 14’ 0” (4267mm) shall be equipped with double end hinges.

- Springs: Oil tempered, helically wound and designed to suit the weight of each door and withstand a minimum n of 10,000 cycles (open/close) over its life.

#### PART 4 – ELECTRICAL OPERATOR AND ACCESSORIES

- The door will be equipped to be operated either by:

- manually with a handle and a sash cord

- or with an electric operator

- Electric operator: Centrally mounted “Trolley” Marantec motor. Silent belt-driven operator, made in Germany.

- Standard accessories: remote control (one) and security photo cell.

- Optional accessories: keypad, wall control panel, etc.

#### PART 5 – INSTALLATION

5.1 Install doors and hardware in accordance with manufacturer's standards.

5.2 Touch-up doors with primer where galvanized finish is damaged during fabrication.

  - Install electrical motors, controller units, push button stations, relays and other electrical equipment required for door operation.

  - Lubricate springs and adjust door operating components to ensure smooth opening and closing of doors.

  - Adjust weather stripping to form weather tight seal against the elements.

# Text boxes

XX